## Slide 1
A 16 Channel Programmable
Constant Fraction Discriminator IC
Bryan Orabutt, MSEE Candidate
Dr. George Engel, ECE Professor
Progress Report
June 15, 2018

## Slide 2: Outline
Features
Specifications and Performance Targets
Process
Layout to Date
Pinout and Configuration Registers
Common Channel
Signal Channel
Summary

## Slide 3: Features
Sixteen CFD (Constant Fraction Discriminator) channels.
Supports signals of both polarities (relative to AGND)
Will accommodate input pulses with 10 – 90 % risetimes from 2 ns to 100 ns.
Leading edge discriminator in each channel has 4-bit programmable threshold
Digital one-shot outputs can be one of 4 (2-bit) programmable widths (50ns, 100 ns, 200ns, 500ns) along with a 5-bit programmable lockout time (100 ns to 3.1 us) to avoid false triggers.
Digital OR and fast analog multiplicity output.

## Slide 4: Design Specifications
Low walk and jitter for input amplitudes from 15 mV to 1.5 V. Performance targets provided on following slide.
Must work correctly with pulse repetition rates up to 1 kHz
Must operate from a single 3.3 – 3.6 Volt supply.
Should include on-chip 3-bit programmable analog signal ground generator (1.65 V +/- 250 mV). Step size approx. 60 mV.
Power consumption not to exceed 250 mW.
Should be packaged in a 64 pin QFP plastic package.

## Slide 5: Performance Targets
Changes to 15 mv to 1.5 V
Changed to 1.5 ns to 50 ns

## Slide 6: IC Process
Austrian Fab House AMS-AG
0.35 micron feature size, 4 metal layers, NWELL
Double poly capacitors
High resistance poly 2 layer (1200 Ohms per square)
Available through MOSIS ($2000 per square mm)
Approximately 4 runs per year
Excellent PDK (Process Design Kit) with digital and analog standard cell libraries
Supports Cadence IC6 tools including Cadence Auto Place and Route and the Silicon Encounter tools.
Models for Monte Carlo simulations provided.

## Slide 7
UNDER CONSTRUCTION!!!!
1.9 X 3.5 mm = 6.6 mm2
Cost of $13,200 (24?) PLUS PACKAGING

## Slide 8: Pinout

## Slide 9: Common Channel
10 uF ext. cap
on AGND pin

## Slide 10: Configuration Registers

## Slide 11: ZTC
12 uA temperature independent current used by the DACs and by the one-shot.

## Slide 12: Channel
Planning on adding one more bit.

## Slide 13: Nowlin
Nowlin delay time constant should be about same value as the the risetime constant.

## Slide 14: Nowlin Circuit
Current Nowlin circuit but there it has PROBLEMS!
The ZC circuit looks like 5 KW for noise purposes.

## Slide 15: PCA

## Slide 16
UNDER CONSTRUCTION!!!!
1.9 X 3.5 mm = 6.6 mm2
Cost of $13,200 (24?) PLUS PACKAGING

## Slide 17: Revised Nowlin Circuit
Current Nowlin circuit but there it has PROBLEMS!
The ZC circuit looks like 5 KW for noise purposes.
Jitter for 3 ns risetime constant will then be about 150 ps (1 sigma) for 15 mV input.
Increase C1 to 20 pF
Have a {2K, 4K} option.
Change to 1K but
Also have a 6K option.

## Slide 18: Time Constants
0.5ns, 1ns, 1.5ns, … 8 ns
OR
3ns, 6ns, 9ns, … 48 ns

## Slide 19: Zero-Cross Detector

## Slide 20: Zero-Cross Detector Amplifier
46 uA

## Slide 21: Walk Performance Summary

## Slide 22: Typical Walk

## Slide 23: Low-Walk Case

## Slide 24: High-Walk Case

## Slide 25: One-Shot
50ns, 100 ns, 200 ns, 500 ns (2 bits)
100 ns to 3.1 us in 100 ns steps (5-bits)

## Slide 26: Current DAC

## Slide 27: 1 Bit of DAC

## Slide 28: DAC Output Stage

## Slide 29: DAC INL

## Slide 30: DAC DNL

## Slide 31: DAC With Low DNL

## Slide 32: DAC with High DNL

## Slide 33: Mutliplicity Buffer
10-90 & risetime of 25 ns
with 10-20 pF load.
Step size is 100 mV.
Compensation capacitor.
2 mA bias

## Slide 34: Summary
We plan to submit the chip in early November!
Much work still needs to be completed!